## Slide 1
Predictive Maintenance Alert
Machine #7 — Temperature Anomaly Report & Recommendations
SkyBridge Manufacturing | Analytics Team | December 2023
ACTION REQUIRED

## Slide 2
Executive Summary
CRITICAL: Machine #7 requires immediate maintenance
Temperature data shows progressive degradation over 6 months, with critical anomaly spikes in the past week. Without intervention, unplanned failure is likely within 24-48 hours.
93.0°C
Last 24h Average
vs normal range of 68-75°C
117.4°C
Peak Recorded
Critical threshold: 85°C
832
Critical Hours (>85°C)
19% of all readings
$600K+
Annual Savings Potential
3 prevented shutdowns/year

## Slide 3
The Evidence: 6 Months of Degradation
What This Means
The 7-day average has crossed the warning threshold and is accelerating upward.
The green-to-red distribution shift shows the machine is running 10-15°C hotter than it was 4 months ago.
This is consistent with bearing wear, coolant degradation, or both.

## Slide 4
Last 7 Days: Imminent Failure Risk
Escalation Timeline
Weeks 1-22
Normal operation, gradual warming trend
Week 23
Intermittent spikes (5-10°C above baseline) — early warnings begin
Week 24-25
Spike frequency and severity increase — 30% of hours show anomalies
Week 26 (Now)
Sustained critical readings — multiple hours above 85°C daily

## Slide 5
Recommendations & ROI
Unplanned Shutdown
$240,000+
$10,000/hr x 24+ hours
Cascading production delays
Emergency parts markup
Overtime labor costs
Planned Maintenance
$40,000
$10,000/hr x 4 hours
Scheduled during off-shift
Standard parts pricing
Regular labor rates
1
Schedule maintenance for Machine #7 within 24 hours
Reduce load immediately, prepare bearing and coolant system replacement parts
TODAY
2
Deploy this monitoring model across all critical machines
Same Excel dashboard + Python pipeline can monitor 50+ machines simultaneously
Q1 2024
3
Integrate with CMMS for automated work orders
When risk score exceeds threshold, auto-generate maintenance tickets in the system
Q2 2024

## Slide 6
Predict the failure.
Prevent the shutdown.
Protect the bottom line.
$200,000 saved per event | 3 events/year | $600,000+ annual impact
Analytics Team | analytics@skybridge-mfg.com